## Slide 1
ELECTRONICS
RMI

## Slide 2: Let’s Recap
Current: Rate of flow of charges
Voltage(Potential difference between two points): Work done per unit charge in moving it from one point to another.
Resistance: Hindrance to the flow of electric current
Capacitance: Ability of a conductor to store charges

## Slide 3: Ohm’s Law
The current flowing through a conductor is directly proportional to the voltage applied across its ends.
V=IR

## Slide 4: Components

## Slide 5: Resistor
Resistors are electronic components which have a specific electrical resistance. The resistor limits the current through a circuit.
Combinations of resistors are also used for voltage division.

## Slide 6: Voltage Divider

## Slide 7: Potentiometer
A potentiometer is basically a potential divider where the ratio of the two resistances can be controlled using a knob.
potentiometers can provide highly precise sensing and measurement for linear or rotary movement as their output voltage is proportional to the wipers position.
It is also used to divide the voltage to the required value.

## Slide 8: Working of Potentiometer

## Slide 9: Photoresistor
An LDR (Light dependent resistor), as its name suggests, offers resistance in response to the ambient light.
The resistance decreases as the intensity of incident light increases, and vice versa. In the absence of light, LDR exhibits a very large resistance.
It can act as a sensor, since a varying voltage drop can be obtained in accordance with the varying light.

## Slide 10: Voltage Regulators
Voltage regulator is a device that maintains the voltage of a power source within acceptable limits(here 5V DC).
Regardless of what kind of load is placed on your circuit, a voltage regulator will always provide a constant, steady output voltage.
Eg: LM-7508 (5v voltage regulator)

## Slide 11: How to use a Voltage Regulator

## Slide 12: Why use Voltage Regulator instead of Voltage Divider?

## Slide 13: Answer:
If the input voltage to a voltage divider fluctuates, the output voltage fluctuates proportionally.
Even if the input voltage to a Voltage Regulator fluctuates, the output stays relatively constant.

## Slide 14: Capacitor
The capacitor is a component which has the ability or “capacity” to store energy in the form of an electrical charge producing a potential difference (Static Voltage) across its plates, much like a small rechargeable battery
It is used to block DC components.

## Slide 15: Diode
It is a semiconductor device with two terminals , allowing the flow of current in one direction only.
It has low resistance in one direction and very high resistance in the other.
It is used in rectifiers to convert AC to DC

## Slide 16: Transistor
A transistor is a semiconductor device used to amplify and switch electronic signals and electrical power respectively. It is composed of semiconductor material and usually has three terminals.

## Slide 17: TRANSISTORS
Transistors can be operated as either amplifier or switch.
Amplifier: It takes in a tiny electric current at one end (an input current) and produces a much bigger electric current (an output current) at the other.
Switch: It can be used as an electric switch rather than the conventional mechanical switch. It can switch on and off millions of times per second. This allows it to be used in computers.
While a mechanical switch would require an actuator to be physically flipped, this switch is controlled by the voltage at the base pin.

## Slide 18: Classification of Transistors
Transistors
BJT
FET
NPN
PNP
JFET
MOSFET
N-Channel
P-Channel
N-Channel
P-Channel

## Slide 19: Bipolar Junction Transistor(BJT)
Being a transistor , BJT is used in current amplification and switching action.
It has three terminals:
  Emitter (Heavily Doped)
  Base (Lightly Doped)
  Collector (Moderately Doped)
It has three different regions of operation:
Active Region
Saturation Region
Cut-off Region

## Slide 20: Types of BJT
PNP Transistor- A ‘N’ type semiconductor is sandwiched between two ‘P’ type semiconductors.
NPN Transistor- A ‘P’ type semiconductor is sandwiched between two ‘N’ type semiconductors.
It carries the name bipolar because the current through the transistor is carried both by holes
(positive) and electrons(negative).

## Slide 21: BJT as Current Amplifier
Bipolar transistors work as current-controlled current regulators. In other words, transistors control the collector current(output current) with respect to the base current(input current).
The emitter current enters the transistor in case of PNP transistor.
The emitter current exits the transistor in case of NPN transistor.
NPN Transistor
input current
output current
PNP Transistor
input current
output current

## Slide 22: MOSFET
The MOSFET (Metal Oxide Semiconductor Field Effect Transistor) is a semiconductor device which is widely used for switching and amplifying electronic signals in the electronic devices. It as low power loss and high efficiency compared to BJT.
It has three terminals:
Source
Drain
Gate

## Slide 23: MOSFET
BJTs are current amplifiers whereas MOSFETs are voltage amplifiers.
MOSFETs are Unipolar devices which means the current flows either due to electrons(N-channel MOSFETs) or holes(P-channel MOSFETs).
For N-channel MOSFET, when the voltage at the gate terminal is increased above a threshold value, current starts to flow between the source and drain.

## Slide 24: Types of MOSFETS

## Slide 25: MOSFET as a Switch(N-channel)
When the button is not pressed, resistor R1 pulls the gate voltage to 0V. Therefore no current flows through the source and drain and therefore the LED is off. When the button is pressed, the gate voltage becomes 5V. So, current flows through the source and drain and the LED glows.

## Slide 26: Bread Board

## Slide 27: Series and Parallel Connections on Breadboard
Parallel Connection
Series Connection

## Slide 28: Pushbutton Connection

## Slide 29: Pull-down Resistor
Pull-down resistors are used in electronic logic circuits to ensure that input settles at logic-0 , if external input is disconnected.
A floating pin picks up noise and interference from the nearby pins. The pull-down resistor dissipates the noises and maintains the potential of the input pin to zero volts (logic-0).

## Slide 30: Pull-up Resistor
Pull-up resistors are used in electronic logic circuits to ensure that input settles at logic- HIGH if external input is disconnected.
Just because you have nothing at all connected to an input pin doesn't mean it is at zero volts. It means the input pin is floating somewhere between low and high.

## Slide 31: MOSFET as a Switch(N-channel)
When the button is not pressed, resistor R1 pulls the gate voltage to 0V. Therefore no current flows through the source and drain and therefore the LED is off. When the button is pressed, the gate voltage becomes 5V. So, current flows through the source and drain and the LED glows.

## Slide 32: Logic Gates using MOSFET

## Slide 33: Logic AND
If both the inputs are HIGH then the output is HIGH. Otherwise, the output is LOW.
MOSFET terminal indication,breadboard connections
New circuit

## Slide 34: Current Amplification using BJT
The circuit uses LDR as a light sensor.
The resistance of the photoresistor changes according to the lighting thus changing the base current.
The small change in base current gets amplified into a large change in collector current, thus changing the brightness of the LED.

## Slide 35: Task
Design OR gate using 2N7000 N-channel MOSFET.

## Slide 37: Logic OR
The output of an OR gate is LOW only when all of its inputs are LOW. Otherwise the output is HIGH.

## Slide 38: Extras

## Slide 39: Logic NOT
The output is logic-0 if the input is logic-1.
The output is logic-1 if the input is logic-0.
X
X’

## Slide 40: Logic NOR
The output of a NOR gate is HIGH only when all of its inputs are LOW. Otherwise the output is LOW.
Symbol | Truth Table |  | 
2-input NOR Gate | B | A | Q
 | 0 | 0 | 1
 | 0 | 1 | 0
 | 1 | 0 | 0
 | 1 | 1 | 0
Boolean Expression Q = A+B | Read as A OR B gives NOT Q |  | 

## Slide 41: Logic NAND
The output of a NAND gate is LOW only when all of its inputs are HIGH. Otherwise the output is HIGH.
Symbol | Truth Table |  | 
2-input NAND Gate | B | A | Q
 | 0 | 0 | 1
 | 0 | 1 | 1
 | 1 | 0 | 1
 | 1 | 1 | 0
Boolean Expression Q = A.B | Read as A AND B gives NOT Q |  | 

## Slide 42: Inverting Comparator Circuit

## Slide 43: Op-Amp Comparator
The Op-amp comparator compares one voltage level with another voltage level, or some preset reference voltage, VREF and produces an output signal based on this voltage comparison.
If V+ > V- then Vout = Vs+
If V+ < V- then Vout = Vs-

## Slide 44: Non-Inverting Comparator Circuit

## Slide 45: Operational Amplifier
An Operational Amplifier, or op-amp for short, is fundamentally a voltage amplifier.
It is used in signal filtering, amplification and also to perform mathematical operations such as addition, subtraction, integration and differentiation.
In this session we will use Op-Amp as a Voltage Comparator
Op-Amp has one output and two inputs:
  Inverting Input
  Non-Inverting Input